## Slide 1
RISC-V RV32I
Instruction
Set
Architecture
Complete Reference — Formats, Encoding & Decoding
47 Base Instructions · 6 Formats · 32×32-bit Registers
R-type
I-type
S-type
B-type
U-type
J-type
What You Will Learn
ISA Overview
Architecture, registers, design philosophy
All 6 Formats
R / I / S / B / U / J bit-field layouts
Every Opcode
All 47 instructions with operations
Field Encoding
opcode, funct3, funct7, rs1, rs2, rd
Sign Extension
How immediates are reconstructed
Full Decoding
Step-by-step decode with real examples
Pseudo-Instrs
How assembler expands shortcuts

## Slide 2
RISC-V Overview — Philosophy, Architecture & Register File
Open standard ISA · 47 base integer instructions · 32 × 32-bit general-purpose registers
Open Standard
No licensing fees. Anyone can implement, extend, or fabricate.
Fixed 32-bit
All RV32I instructions are exactly 4 bytes. No variable-length encoding.
32 Registers
x0–x31 each 32 bits wide. x0 is hardwired to 0 always.
Load/Store
Only LW/SW touch memory. All computation happens in registers.
6 Formats
R I S B U J — each defines where fields live in the 32-bit word.
Modular ISA
RV32I is base. Add M(multiply), F(float), V(vector) extensions.
Register
ABI
Purpose
x0
zero
Always 0 — hardwired
x1
ra
Return address
x2
sp
Stack pointer
x3
gp
Global pointer
x4
tp
Thread pointer
x5-7
t0-2
Temporaries
x8
s0/fp
Saved / frame ptr
x9
s1
Saved register
x10-11
a0-1
Fn args / return values
x12-17
a2-7
Function arguments
x18-27
s2-11
Saved registers
x28-31
t3-6
Temporaries
All RV32I addresses are 32-bit byte addresses · Little-endian byte order

## Slide 3
All 6 Instruction Formats — How 32 Bits Are Divided
Every RV32I instruction fits one of these 6 templates. Fields rs1, rs2, rd, funct3 stay in the same positions across formats.
31
28
24
20
16
12
8
4
0
R-type
funct7
7b
rs2
5b
rs1
5b
funct3
3b
rd
5b
opcode
7b
ADD SUB AND OR XOR SLL SRL SRA SLT SLTU
I-type
imm[11:0]
12b
rs1
5b
funct3
3b
rd
5b
opcode
7b
ADDI LW LH LB JALR SLLI SRLI SRAI SLTI XORI
S-type
imm[11:5]
7b
rs2
5b
rs1
5b
funct3
3b
imm[4:0]
5b
opcode
7b
SW SH SB
B-type
imm[12|10:5]
7b
rs2
5b
rs1
5b
funct3
3b
imm[4:1|11]
5b
opcode
7b
BEQ BNE BLT BGE BLTU BGEU
U-type
imm[31:12]
20b
rd
5b
opcode
7b
LUI AUIPC
J-type
imm[20|10:1|11|19:12]
20b
rd
5b
opcode
7b
JAL
opcode
rs1/rs2
rd
funct7/3
immediate

## Slide 4
R-Type Format — Register-Register Operations
opcode=0110011 (0x33) · funct7 + funct3 select exact operation · no immediate
Format:
funct7
7b
rs2
5b
rs1
5b
funct3
3b
rd
5b
opcode
7b
31
0
← bit positions →
Decode: ADD x12, x10, x11 (machine code = 0x00B50633)
Binary: 0000 0000 1011 0101 0 000 0110 0 011 0011
0000000
funct7=0
01011
rs2=x11
01010
rs1=x10
000
funct3=0
01100
rd=x12
0110011
opcode
▲ opcode=0x33 → R-type
▲ rd=01100 → x12
▲ funct3=000 → ADD
▲ rs1=01010 → x10
▲ rs2=01011 → x11
▲ funct7=0000000 → ADD (not SUB)
Instr
opcode
funct3
funct7
Operation
ADD
0110011
000
0000000
rd = rs1 + rs2
SUB
0110011
000
0100000
rd = rs1 - rs2
AND
0110011
111
0000000
rd = rs1 & rs2
OR
0110011
110
0000000
rd = rs1 | rs2
XOR
0110011
100
0000000
rd = rs1 ^ rs2
SLL
0110011
001
0000000
rd = rs1 << rs2[4:0]
SRL
0110011
101
0000000
rd = rs1 >> rs2[4:0] (logical)
SRA
0110011
101
0100000
rd = rs1 >>> rs2[4:0] (arithmetic)
SLT
0110011
010
0000000
rd = (rs1 < rs2) ? 1 : 0 (signed)
SLTU
0110011
011
0000000
rd = (rs1 < rs2) ? 1 : 0 (unsigned)
Result: x12 = x10 + x11 = value in x10 + value in x11
Note: ADD vs SUB only differ in funct7[5] = 0 vs 1

## Slide 5
I-Type Format — Immediate, Load & JALR
12-bit signed immediate · used for arithmetic with immediate, loads, and JALR · sign-extended to 32 bits
Format:
imm[11:0]
12b
rs1
5b
funct3
3b
rd
5b
opcode
7b
31
0
← bit positions →
Decode: ADDI x5, x6, -4 (machine code = 0xFFC30293)
Binary: 1111 1111 1100 0011 0 000 0010 1 001 0011
111111111100
imm[11:0]=-4
00110
rs1=x6
000
funct3=ADDI
00101
rd=x5
0010011
opcode=0x13
▲ opcode=0x13 → I-type arith
▲ rd=00101 → x5
▲ funct3=000 → ADDI
▲ rs1=00110 → x6
▲ imm=111111111100 → sign-ext → -4
Sign Extension
12-bit imm → 32 bits by replicating bit[11]
111111111100 (12-bit) = -4
→ 0xFFFFFFFC (-4 as 32-bit signed)
Used by: ADDI, LW, LH, LB, JALR, shifts
Instr
opcode
funct3
Description / Operation
ADDI
0010011
000
rd = rs1 + sext(imm12)
SLTI
0010011
010
rd = (rs1 < sext(imm)) ? 1:0 signed
ANDI
0010011
111
rd = rs1 & sext(imm)
ORI
0010011
110
rd = rs1 | sext(imm)
XORI
0010011
100
rd = rs1 ^ sext(imm)
SLLI
0010011
001
rd = rs1 << shamt (imm[4:0])
SRLI
0010011
101
rd = rs1 >> shamt (logical)
SRAI
0010011
101
rd = rs1 >>> shamt (arith; imm[10]=1)
LW
0000011
010
rd = Mem32[rs1 + sext(imm)]
LH
0000011
001
rd = sext(Mem16[rs1+sext(imm)])
LB
0000011
000
rd = sext(Mem8[rs1+sext(imm)])
LHU
0000011
101
rd = zext(Mem16[rs1+sext(imm)])
LBU
0000011
100
rd = zext(Mem8[rs1+sext(imm)])
JALR
1100111
000
rd=PC+4; PC=(rs1+sext(imm))&~1

## Slide 6
S-Type & B-Type Formats — Stores and Conditional Branches
S-type: immediate is SPLIT across two fields to keep rs1/rs2/funct3 aligned · B-type: immediate is bit-scrambled for same reason
S-TYPE — Store Instructions (SW, SH, SB)
imm[11:5]
7b
rs2
5b
rs1
5b
funct3
3b
imm[4:0]
5b
opcode
7b
Decode: SW x5, -8(x6) [Store x5 to address (x6 + (-8))] = 0xFE532C23
1111111
imm[11:5]
00101
rs2=x5
00110
rs1=x6
010
funct3=2
11000
imm[4:0]
0100011
opcode
Reassemble imm: {imm[11:5], imm[4:0]} = {1111111, 11000} = 111111111000 = -8
S-Type splits the immediate to keep rs1/rs2 in the same bit positions as R-type — hardware decoder stays simple.
B-TYPE — Conditional Branch Instructions (BEQ, BNE, BLT, BGE…)
imm[12|10:5]
7b
rs2
5b
rs1
5b
funct3
3b
imm[4:1|11]
5b
opcode
7b
Decode: BEQ x10, x11, +16 [Branch +16 bytes if x10==x11] = 0x00B50863
0000000
imm[12|10:5]
01011
rs2=x11
01010
rs1=x10
000
funct3=BEQ
10000
imm[4:1|11]
1100011
opcode
Reassemble: imm[12]=0, imm[11]=1, imm[10:5]=000000, imm[4:1]=1000, imm[0]=0 → 0 0001 0000 0 = +16
B-type offset is in units of 2 (LSB is always 0 — branches target 2-byte aligned addresses). Max range: ±4 KB.

## Slide 7
U-Type & J-Type Formats — Upper Immediate & Unconditional Jump
U-type: 20-bit immediate placed in bits[31:12] · J-type: 21-bit PC-relative offset, bit-scrambled
U-TYPE — Upper Immediate (LUI, AUIPC)
imm[31:12]
20b
rd
5b
opcode
7b
Decode: LUI x10, 0x12345 [x10 = 0x12345000] = 0x123450B7
00010010001101000101
imm[31:12]=0x12345
01010
rd=x10
0110111
opcode=LUI
Result: x10 = 0x12345 << 12 = 0x12345000. Lower 12 bits always zero. AUIPC adds PC instead.
Mnemonic
opcode
Operation
Use Case
LUI
0110111
rd = imm[31:12] << 12
Load 32-bit constant (upper 20 bits)
AUIPC
0010111
rd = PC + (imm[31:12] << 12)
PC-relative addressing / CALL setup
J-TYPE — Unconditional Jump (JAL)
imm[20|10:1|11|19:12]
20b
rd
5b
opcode
7b
Decode: JAL x1, +100 [Jump +100 bytes, save PC+4 into x1] = 0x064000EF
00000110010000000000
imm scrambled
00001
rd=x1 (ra)
1101111
opcode=JAL
J-type bit scramble: instr[31]→imm[20], instr[30:21]→imm[10:1], instr[20]→imm[11], instr[19:12]→imm[19:12], imm[0]=0. Max range: ±1 MB.

## Slide 8
RV32I Opcode Map — Decoding opcode[6:0]
All RV32I opcodes end in 11 (bits[1:0]=11). The 5 bits above select the instruction class.
Step 1 in decoding: read bits[6:0] of the instruction word.
0110011
0x33
R-type (ALU)
ADD SUB AND OR XOR SLL SRL SRA SLT SLTU
0010011
0x13
I-type (Arith)
ADDI SLTI ANDI ORI XORI SLLI SRLI SRAI
0000011
0x03
I-type (Load)
LW LH LB LHU LBU
0100011
0x23
S-type (Store)
SW SH SB
1100011
0x63
B-type (Branch)
BEQ BNE BLT BGE BLTU BGEU
0110111
0x37
U-type LUI
LUI — Load Upper Immediate
0010111
0x17
U-type AUIPC
AUIPC — Add Upper Immediate to PC
1101111
0x6F
J-type JAL
JAL — Jump And Link
1100111
0x67
I-type JALR
JALR — Jump And Link Register
1110011
0x73
SYSTEM
ECALL EBREAK (and CSR instructions)
0001111
0x0F
MISC-MEM
FENCE FENCE.I — memory ordering

## Slide 9
Complete Instruction Reference — Arithmetic, Logic & Shifts
R-type and I-type arithmetic · all share opcode 0110011 (R) or 0010011 (I)
ARITHMETIC — R-type (opcode=0110011)
Mnemonic
Operation
opcode
funct3
funct7
Notes
ADD
rd = rs1 + rs2
0110011
000
0000000
Signed/unsigned add
SUB
rd = rs1 - rs2
0110011
000
0100000
funct7[5]=1 distinguishes from ADD
ADDI
rd = rs1 + sext(imm12)
0010011
000
—
I-type; no SUBI (use ADDI with -imm)
LOGIC — R-type
Mnemonic
Operation
opcode
funct3
funct7
Notes
AND
rd = rs1 & rs2
0110011
111
0000000
Bitwise AND
OR
rd = rs1 | rs2
0110011
110
0000000
Bitwise OR
XOR
rd = rs1 ^ rs2
0110011
100
0000000
Bitwise XOR
ANDI
rd = rs1 & sext(imm)
0010011
111
—
AND immediate
ORI
rd = rs1 | sext(imm)
0010011
110
—
OR immediate
XORI
rd = rs1 ^ sext(imm)
0010011
100
—
XOR immediate
SHIFTS
Mnemonic
Operation
opcode
funct3
funct7
Notes
SLL
rd = rs1 << rs2[4:0]
0110011
001
0000000
Logical shift left
SRL
rd = rs1 >> rs2[4:0]
0110011
101
0000000
Logical shift right (zero-fill)
SRA
rd = rs1 >>> rs2[4:0]
0110011
101
0100000
Arithmetic right (sign-fill)
SLLI
rd = rs1 << shamt
0010011
001
000000x
shamt = imm[4:0]
SRLI
rd = rs1 >> shamt
0010011
101
0000000
shamt = imm[4:0]
SRAI
rd = rs1 >>> shamt
0010011
101
0100000
shamt = imm[4:0], imm[10]=1

## Slide 10
Complete Instruction Reference — Memory, Branch & Control Flow
Load/Store access memory · Branches use PC-relative offset · JAL/JALR for calls
LOADS — I-type (opcode=0000011)
Mnemonic
Operation
opcode
funct3
funct7
Notes
LW
rd = Mem32[rs1+sext(imm)]
0000011
010
—
Load 32-bit word
LH
rd = sext(Mem16[rs1+sext(imm)])
0000011
001
—
Load 16-bit signed half-word
LB
rd = sext(Mem8[rs1+sext(imm)])
0000011
000
—
Load 8-bit signed byte
LHU
rd = zext(Mem16[rs1+sext(imm)])
0000011
101
—
Load 16-bit unsigned
LBU
rd = zext(Mem8[rs1+sext(imm)])
0000011
100
—
Load 8-bit unsigned
STORES — S-type (opcode=0100011)
Mnemonic
Operation
opcode
funct3
funct7
Notes
SW
Mem32[rs1+sext(imm)] = rs2
0100011
010
—
Store 32-bit word
SH
Mem16[rs1+sext(imm)] = rs2[15:0]
0100011
001
—
Store low 16 bits
SB
Mem8[rs1+sext(imm)] = rs2[7:0]
0100011
000
—
Store low 8 bits
BRANCHES — B-type (opcode=1100011)
Mnemonic
Operation
opcode
funct3
funct7
Notes
BEQ
if (rs1==rs2) PC+=sext(imm)
1100011
000
—
Branch if equal
BNE
if (rs1!=rs2) PC+=sext(imm)
1100011
001
—
Branch if not equal
BLT
if (rs1<rs2) PC+=sext(imm)
1100011
100
—
Branch less than (signed)
BGE
if (rs1>=rs2) PC+=sext(imm)
1100011
101
—
Branch greater/equal (signed)
BLTU
if (rs1<rs2) PC+=sext(imm)
1100011
110
—
Branch less than (unsigned)
BGEU
if (rs1>=rs2) PC+=sext(imm)
1100011
111
—
Branch greater/equal (unsigned)
UPPER IMMEDIATE + JUMP + SYSTEM
Mnemonic
Operation
opcode
funct3
funct7
Notes
LUI
rd = imm[31:12]<<12
0110111
—
—
Load upper 20 bits
AUIPC
rd = PC + imm[31:12]<<12
0010111
—
—
PC-relative upper imm
JAL
rd=PC+4; PC+=sext(imm21)
1101111
—
—
Unconditional jump (J-type)
JALR
rd=PC+4; PC=(rs1+sext(imm))&~1
1100111
000
—
Jump register (I-type)
ECALL
Environment call
1110011
000
—
Syscall to OS
EBREAK
Debug breakpoint
1110011
000
—
Trap to debugger

## Slide 11
funct3 & funct7 — The Sub-Opcode Fields
Multiple instructions share the same opcode · funct3 (3 bits) and funct7 (7 bits) disambiguate them
Why sub-opcode fields?
The 7-bit opcode field would only give 128 unique instructions. By adding funct3 (3 bits) and funct7 (7 bits), each opcode class can encode up to 8 × 128 = 1024 variants — keeping the ISA extensible without wasting opcode space.
funct3 Encoding (R-type, opcode=0110011)
funct3
funct7=0000000
funct7=0100000
000
ADD
SUB
001
SLL
—
010
SLT
—
011
SLTU
—
100
XOR
—
101
SRL
SRA
110
OR
—
111
AND
—
funct3 for Branches (opcode=1100011)
funct3
Instruction
Condition
000
BEQ
rs1 == rs2
001
BNE
rs1 != rs2
100
BLT
rs1 < rs2 (signed)
101
BGE
rs1 >= rs2 (signed)
110
BLTU
rs1 < rs2 (unsigned)
111
BGEU
rs1 >= rs2 (unsigned)
funct7 bit[5] — The Critical Toggle
ADD and SUB share funct3=000. Only funct7[5] differs:
funct7 = 0000000 → ADD
funct7 = 0100000 → SUB
Same trick for SRL vs SRA (funct3=101):
funct7 = 0000000 → SRL (logical)
funct7 = 0100000 → SRA (arithmetic)
Shift Immediate Encoding (SLLI/SRLI/SRAI)
I-type with special immediate layout:
instr[31:25] = 0000000 or 0100000 (func7)
instr[24:20] = shamt[4:0] (shift amount 0-31)
instr[19:15] = rs1
instr[14:12] = 001(SLL) 101(SRL/SRA)
SLLI x1, x2, 3:
imm[11:0] = 000000 00011
^^^^^^ ↑↑↑↑↑
funct7 shamt=3

## Slide 12
Immediate Value Encoding — All 5 Formats Compared
Each format encodes its immediate in a different bit layout · all sign-extended from instr[31]
I-type imm
Source bits: instr[31:20]
12-bit signed. Range: -2048 to +2047.
Used by: ADDI LW LH LB JALR SLTI
imm = { {20{instr[31]}}, instr[31:20] }
S-type imm
Source bits: instr[31:25] ++ instr[11:7]
12-bit signed (split across two fields).
Used by: SW SH SB
imm = { {20{instr[31]}}, instr[31:25], instr[11:7] }
B-type imm
Source bits: imm[12|10:5] imm[4:1|11] (scrambled)
13-bit signed, LSB always 0 (×2 scale).
Used by: BEQ BNE BLT BGE BLTU BGEU
imm = { {19{instr[31]}}, instr[31], instr[7], instr[30:25], instr[11:8], 1'b0 }
U-type imm
Source bits: instr[31:12]
20-bit unsigned, placed in bits[31:12].
Used by: LUI AUIPC
imm = { instr[31:12], 12'b0 } (lower 12 always zero)
J-type imm
Source bits: imm[20|10:1|11|19:12] (scrambled)
21-bit signed, LSB always 0 (×2 scale).
Used by: JAL
imm = { {11{instr[31]}}, instr[31], instr[19:12], instr[20], instr[30:21], 1'b0 }
Key insight: ALL immediates are sign-extended from bit[31] of the instruction. The scrambling exists solely to keep rs1, rs2, and funct3 in the same bit positions across all formats — simplifying the decoder hardware.

## Slide 13
Step-by-Step Decode #1 — LW x14, 12(x2)
Machine code: 0x00C12703 · Load 32-bit word from memory address (sp + 12) into x14
Binary: 0000 0000 1100 0001 0010 0111 0 0000 011
000000001100
imm[11:0]=12
00010
rs1=x2(sp)
010
funct3=LW
01110
rd=x14
0000011
opcode=LOAD
Step 1
Read opcode[6:0]
= 0000011 = 0x03
Look up: 0x03 = LOAD family (I-type)
Step 2
Read funct3[14:12]
= 010
Look up: 010 = LW (load 32-bit word)
Step 3
Read rd[11:7]
= 01110 = 14
Destination register: x14
Step 4
Read rs1[19:15]
= 00010 = 2
Base address register: x2 (= sp)
Step 5
Read imm[31:20]
= 000000001100
Sign-extend 12 bits → +12 (0x0000000C)
Step 6
Compute address
EA = x2 + 12 = sp + 12
Execute
Load word from memory
x14 = Mem32[EA] = Mem32[sp + 12]

## Slide 14
Step-by-Step Decode #2 — BNE x5, x6, -20
Machine code: 0xFE629EE3 · Branch -20 bytes if x5 ≠ x6 (B-type, scrambled immediate)
Binary: 1111 1110 0110 0010 1 001 0110 1 110 0011
1111111
imm[12|10:5]
00110
rs2=x6
00101
rs1=x5
001
funct3=BNE
01101
imm[4:1|11]
1100011
opcode=BR
B-type Immediate Bit Reconstruction:
From the instruction bits:
instr[31] → imm[12] = 1
instr[7] → imm[11] = 1
instr[30:25] → imm[10:5] = 111111
instr[11:8] → imm[4:1] = 0110
imm[0] → always 0
Assembled: imm = 1_1_111111_0110_0
= 1111111101100
= 0xFFFFFFEC = -20 (sign-extended 13-bit value)
Final: if (x5 != x6) then PC = PC + (-20)
PC steps back 20 bytes
= 5 instructions back
(each instruction = 4 bytes)
If x5 == x6, branch NOT taken → PC += 4 (next instruction)
Step 1
opcode = 1100011 = 0x63
→ BRANCH class (B-type)
Result: → BRANCH class (B-type)
Step 2
funct3 = 001
→ BNE (branch if NOT equal)
Result: → BNE (branch if NOT equal)
Step 3
rs1[19:15] = 00101
→ rs1 = x5
Result: → rs1 = x5
Step 4
rs2[24:20] = 00110
→ rs2 = x6
Result: → rs2 = x6
Step 5
Reconstruct imm (see above)
→ offset = -20
Result: → offset = -20
Execute
Compare: x5 != x6 ?
If yes: PC = PC + (-20). If no: PC += 4
Result: If yes: PC = PC + (-20). If no: PC += 4

## Slide 15
Step-by-Step Decode #3 — JAL x1, +100
Machine code: 0x064000EF · Jump +100 bytes, save return address in x1 (ra)
Binary: 0000 0110 0100 0000 0000 0000 1 110 1111
00000110010000000000
imm scrambled
00001
rd=x1(ra)
1101111
opcode=JAL
J-type Immediate Bit Reconstruction (most complex format):
Raw 20-bit immediate field from instr[31:12]:
0000 0110 0100 0000 0000
Extract bits:
instr[31] → imm[20] = 0
instr[19:12] → imm[19:12] = 00000000
instr[20] → imm[11] = 0
instr[30:21] → imm[10:1] = 0011001000 (= 50 decimal × 2 = 100)
Assembled: 0_00000000_0_0011001000_0
= 0000 0000 0001 1001 0000
= 0x00000064 = +100 bytes
Why scrambled?
The bit scrambling keeps the
sign bit (imm[20]) in instr[31]
for all formats — hardware
sign-extender is one-bit wide.
All other bits moved to overlap
with B-type positions where
possible, sharing decode logic.
Step 1: opcode=1101111=0x6F
J-type format confirmed
Step 2: rd=00001
Destination = x1 (return address register ra)
Step 3: reconstruct imm
offset = +100 bytes (25 instructions forward)
Execute
x1 = PC + 4 (save return address)
PC = PC + 100 (jump forward)

## Slide 16
Step-by-Step Decode #4 — SW x5, -8(x6)
Machine code: 0xFE532C23 · Store 32-bit value of x5 to memory at (x6 - 8) · S-type split immediate
Binary: 1111 1110 0101 0011 0 010 1100 0 010 0011
1111111
imm[11:5]
00101
rs2=x5
00110
rs1=x6
010
funct3=SW
11000
imm[4:0]
0100011
opcode
S-type Immediate Reconstruction (split across two fields):
imm[11:5] = instr[31:25] = 1111111 (upper 7 bits)
imm[4:0] = instr[11:7] = 11000 (lower 5 bits)
Concatenate: {imm[11:5], imm[4:0]} = 1111111 11000
= 111111111000 (12-bit two's complement)
= -8 (0xFFFFFFF8 sign-extended to 32 bits)
Step 1
opcode = 0100011 = 0x23
→ STORE class (S-type)
Effective: → STORE class (S-type)
Step 2
funct3 = 010
→ SW (store 32-bit word)
Effective: → SW (store 32-bit word)
Step 3
rs1[19:15] = 00110
→ base address register x6
Effective: → base address register x6
Step 4
rs2[24:20] = 00101
→ data to store is from x5
Effective: → data to store is from x5
Step 5
Reconstruct imm = -8
→ offset from base
Effective: → offset from base
Execute
EA = x6 + (-8)
Mem32[EA] = x5 (write 4 bytes)
Effective: Mem32[EA] = x5 (write 4 bytes)

## Slide 17
Pseudo-Instructions — Assembler Shortcuts
These are NOT in the hardware. The assembler expands them into real RV32I instructions before encoding.
Pseudo
Expands To
Hex (NOP)
Explanation
NOP
ADDI x0, x0, 0
0x00000013
No operation — writes x0 (discarded)
MV rd, rs
ADDI rd, rs, 0
varies
Copy register
LI rd, imm
LUI+ADDI (or just ADDI)
varies
Load any 32-bit immediate
NOT rd, rs
XORI rd, rs, -1
varies
-1 = 0xFFF in 12-bit signed
NEG rd, rs
SUB rd, x0, rs
varies
Negate: rd = 0 - rs
SEQZ rd, rs
SLTIU rd, rs, 1
varies
Set if equal zero
SNEZ rd, rs
SLTU rd, x0, rs
varies
Set if not equal zero
BEQZ rs, lbl
BEQ rs, x0, lbl
varies
Branch if rs == 0
BNEZ rs, lbl
BNE rs, x0, lbl
varies
Branch if rs != 0
J offset
JAL x0, offset
varies
Jump, discard return address
JR rs
JALR x0, rs, 0
varies
Jump to register
RET
JALR x0, x1, 0
varies
Return: jump to address in ra (x1)
CALL func
AUIPC x1, hi(func)
JALR x1, lo(func)(x1)
varies
Function call (2 instrs)
LA rd, symbol
AUIPC rd, hi
ADDI rd, rd, lo
varies
Load address of symbol

## Slide 18
Instruction Encoding Examples — Assembly to Machine Code
How to manually encode any RV32I instruction from the ISA spec
ADD R1, R2, R3
0x00310033
R-type
0000000_00011_00010_000_00001_0110011
• funct7=0000000
• rs2=x3=00011
• rs1=x2=00010
• funct3=000
• rd=x1=00001
• opcode=0110011
ADDI x5, x6, -4
0xFFC30293
I-type
111111111100_00110_000_00101_0010011
• imm[11:0]=-4=FFC
• rs1=x6=00110
• funct3=000
• rd=x5=00101
• opcode=0010011
LW x14, 12(x2)
0x00C12703
I-type
000000001100_00010_010_01110_0000011
• imm=+12=00C
• rs1=x2=00010
• funct3=010
• rd=x14=01110
• opcode=0000011
SW x5, -8(x6)
0xFE532C23
S-type
1111111_00101_00110_010_11000_0100011
• imm[11:5]=1111111
• rs2=x5=00101
• rs1=x6=00110
• funct3=010
• imm[4:0]=11000
• opcode=0100011
BEQ x10,x11,+16
0x00B50863
B-type
0_000000_01011_01010_000_1000_0_1100011
• imm[12|10:5]=0000000
• rs2=x11
• rs1=x10
• funct3=000
• imm[4:1|11]=10000
• opcode=1100011
LUI x10, 0x12345
0x123450B7
U-type
00010010001101000101_01010_0110111
• imm[31:12]=0x12345=00010010001101000101
• rd=x10=01010
• opcode=0110111

## Slide 19
General Decoding Algorithm — Step by Step
Apply this procedure to decode any RV32I 32-bit machine word
Read bits[6:0]
= opcode field
opcode[1:0]
== 11 ?
NO → Compressed
(RV32C ext)
YES
Look up opcode[6:2]
in format table
Identify Format:
R-type
read rs1,rs2,rd
funct3,funct7
compute
I-type
read rs1,rd
funct3,imm[11:0]
sign-extend imm
S-type
read rs1,rs2
funct3
recombine imm
B-type
read rs1,rs2
funct3
scrambled imm×2
U-type
read rd
imm[31:12]
shift left 12
J-type
read rd
scrambled imm×2
PC-relative
Extract register addresses
rd, rs1, rs2
Execute / Update PC

## Slide 20
Key Takeaways & Quick Reference Card
Everything you need to decode any RV32I instruction from scratch
01
All instructions are exactly 32 bits
Fixed-width: fetch is always 4 bytes. PC increments by 4 each cycle.
02
6 formats — opcode[6:0] identifies which
0x33=R, 0x13/0x03/0x67=I, 0x23=S, 0x63=B, 0x37/0x17=U, 0x6F=J
03
rs1, rs2, funct3 stay in fixed positions
Hardware decoder reads these bits the same way regardless of format.
04
Immediates always sign-extend from bit[31]
Every format puts the sign bit at instr[31]. One extender for all.
05
B and J immediates have implicit ×2 scale
imm[0] is always 0 — branch/jump targets are 2-byte aligned.
06
funct7[5] differentiates ADD/SUB, SRL/SRA
Two instructions sharing opcode+funct3 flip only one bit of funct7.
07
x0 is always 0 — writes are discarded
NOP = ADDI x0,x0,0. MV = ADDI rd,rs,0. Key for pseudo-instructions.
08
47 base instructions, easily extensible
RV32I is the minimal starting point. M/A/F/D/V/C extensions add capabilities.
RISC-V RV32I · 6 Formats · 47 Instructions · 32 Registers · Fixed 32-bit encoding · Open Standard