## Slide 1
Single-Cycle CPU
Datapath & RTL Design
RISC-V Architecture & FPGA Design Training
Program Counter · Register File · ALU · Control Unit · RTL Simulation
Single-Cycle
RTL Coding
Simulation
Today's Agenda
▶ Single-Cycle Datapath
▶ Control Signals & CU
Program Counter RTL
Register File (32×32)
ALU Implementation
Immediate Generator
Core RTL Modules
Simulation & Debug

## Slide 2
Single-Cycle Datapath — Complete Architecture Overview
Instruction
Memory
Register
File
Sign
Extend
ALU
Data
Memory
MUX
WB
PC
PC+4 / Branch
Adder
ALUSrc
MUX
Control
Unit
PC addr
instr[31:0]
rs1,rs2
imm
EA/result
mem_out
→ rd
Instruction Data Flows:
▸ R-type: RegFile → ALU → RegFile
▸ I-type (LW): RegFile → ALU(EA) → Mem → RegFile
▸ S-type (SW): RegFile → ALU(EA) → Mem
▸ B-type: RegFile → ALU(compare) → PC

## Slide 3
Datapath Components — Function of Each Block
📍 Program Counter (PC)
Holds address of current instruction
32-bit register clocked on posedge
Outputs PC to Instruction Memory
Updates: PC+4 or branch target
🗃️ Instruction Memory
Read-only memory storing the program
Addressed by PC[31:2]
Outputs 32-bit instruction word
Typically synchronous SRAM in FPGA
📋 Register File (32×32)
32 general-purpose 32-bit registers
2 async read ports (rs1, rs2)
1 sync write port (rd, clk)
x0 is hardwired to 0 always
🔢 Sign Extender
Expands 12-bit immediate to 32 bits
Replicates bit[11] into bits[31:12]
Essential for ADDI, LW, SW, branches
Combinational — zero latency
⚙️ ALU
Performs arithmetic and logic ops
ADD, SUB, AND, OR, XOR, SLT
Outputs: 32-bit result + zero flag
zero flag drives branch control
💾 Data Memory
SRAM for load/store instructions
Write-enable controlled by MemWrite
Read-enable controlled by MemRead
Word-aligned 32-bit access

## Slide 4
Control Signals & Control Unit — The Decision Engine
Control Signal Truth Table
Signal
R-type
LW
SW
BEQ
JAL
RegWrite
1
1
0
0
1
MemRead
0
1
0
0
0
MemWrite
0
0
1
0
0
ALUSrc
0
1
1
0
0
Branch
0
0
0
1
0
Jump
0
0
0
0
1
MemToReg
0
1
0
0
0
ALUOp[1:0]
10
00
00
01
00
Control Unit — Verilog
SV
module control_unit (
input [6:0] opcode,
output reg RegWrite, MemRead,
output reg MemWrite, ALUSrc,
output reg Branch, Jump,
output reg MemToReg,
output reg [1:0] ALUOp
);
always_comb begin
// Default: all off
{RegWrite,MemRead,MemWrite,
ALUSrc,Branch,Jump,
MemToReg} = 7'b0;
ALUOp = 2'b00;
case (opcode)
7'b0110011: // R-type
{RegWrite,ALUOp}={1'b1,2'b10};
7'b0000011: // LW (I-type)
{RegWrite,MemRead,ALUSrc,
MemToReg}=4'b1111;
7'b0100011: // SW (S-type)
{MemWrite,ALUSrc}=2'b11;
7'b1100011: // BEQ (B-type)
{Branch,ALUOp}={1'b1,2'b01};
7'b1101111: // JAL
{RegWrite,Jump}=2'b11;
default: ; // NOP
endcase
end
endmodule

## Slide 5
Program Counter Design — RTL Implementation
What it does
Stores the address of the current instruction.
Every clock cycle it updates to the next PC value.
Next PC logic
Normal: PC_next = PC + 4
Branch taken: PC_next = PC + imm_offset
JAL: PC_next = PC + J-imm
Reset
On reset, PC loads 0x00000000 (or boot vector)
This is the first instruction address fetched.
Timing
PC register: always_ff (clocked)
PC adder (+4): always_comb (combinational)
MUX selection: combinational on Branch signal
SV
// ─── Program Counter Module ───────────────
module pc_register (
input logic clk, rst,
input logic [31:0] pc_next,
output logic [31:0] pc
);
always_ff @(posedge clk) begin
if (rst) pc <= 32'h0000_0000;
else pc <= pc_next;
end
endmodule
// ─── PC Adder (+4) ───────────────────────
module pc_adder (
input logic [31:0] pc,
output logic [31:0] pc_plus4
);
assign pc_plus4 = pc + 32'd4;
endmodule
// ─── Branch/Jump MUX ─────────────────────
module pc_mux (
input logic [31:0] pc_plus4,
input logic [31:0] branch_tgt,
input logic [31:0] jump_tgt,
input logic branch_taken,
input logic jump,
output logic [31:0] pc_next
);
always_comb begin
if (jump) pc_next = jump_tgt;
else if (branch_taken) pc_next = branch_tgt;
else pc_next = pc_plus4;
end
endmodule

## Slide 6
Register File (32×32) — RTL Design
Register File Architecture
32 × 32-bit
Registers
x0=0
x1=ra
x2=sp
...
x31=t6
rs1 [4:0] →
rs2 [4:0] →
rd [4:0] →
wd [31:0] →
we →
clk →
← rd1 [31:0]
← rd2 [31:0]
SV
module register_file (
input logic clk,
input logic [4:0] rs1, rs2, // read addrs
input logic [4:0] rd, // write addr
input logic we, // write enable
input logic [31:0] wd, // write data
output logic [31:0] rd1, rd2 // read data
);
// 32 registers of 32 bits each
logic [31:0] regs [0:31];
// Asynchronous read (combinational)
// x0 is always 0 — hardwired
assign rd1 = (rs1 == 5'b0) ? 32'b0 : regs[rs1];
assign rd2 = (rs2 == 5'b0) ? 32'b0 : regs[rs2];
// Synchronous write (clocked)
always_ff @(posedge clk) begin
if (we && (rd != 5'b0))
regs[rd] <= wd;
// x0 is never written — guard ensures this
end
// Initialize for simulation
initial begin
for (int i = 0; i < 32; i++)
regs[i] = 32'h0;
end
endmodule

## Slide 7
ALU Implementation — Arithmetic Logic Unit RTL
ALU Operations & Control Encoding
ALUCtrl
Operation
Instruction
4'b0000
ADD a + b
ADD, ADDI, LW, SW
4'b0001
SUB a - b
SUB, BEQ (compare)
4'b0010
AND a & b
AND, ANDI
4'b0011
OR a | b
OR, ORI
4'b0100
XOR a ^ b
XOR, XORI
4'b0101
SLT a<b
SLT, SLTI (signed)
4'b0110
SLL a<<b
SLL, SLLI
4'b0111
SRL a>>b
SRL, SRLI (logical)
4'b1000
SRA a>>>b
SRA, SRAI (arith)
zero = (result == 32'b0) → used by BEQ/BNE branch control
SV
module alu (
input logic [31:0] a, b,
input logic [3:0] alu_ctrl,
output logic [31:0] result,
output logic zero // BEQ flag
);
always_comb begin
case (alu_ctrl)
4'b0000: result = a + b; // ADD
4'b0001: result = a - b; // SUB
4'b0010: result = a & b; // AND
4'b0011: result = a | b; // OR
4'b0100: result = a ^ b; // XOR
4'b0101: result = {{31{1'b0}},
($signed(a)<$signed(b))}; // SLT
4'b0110: result = a << b[4:0]; // SLL
4'b0111: result = a >> b[4:0]; // SRL
4'b1000: result = $signed(a)>>>
b[4:0]; // SRA
default: result = 32'hx;
endcase
end
assign zero = (result == 32'b0);
endmodule
// ─── ALU Control Decoder ──────────────────
module alu_control (
input logic [1:0] ALUOp,
input logic [2:0] funct3,
input logic funct7_5,
output logic [3:0] alu_ctrl
);
always_comb begin
case (ALUOp)
2'b00: alu_ctrl = 4'b0000; // ADD (LW/SW)
2'b01: alu_ctrl = 4'b0001; // SUB (BEQ)
2'b10: // R-type: use funct3/funct7
case (funct3)
3'b000: alu_ctrl = funct7_5 ?
4'b0001 : 4'b0000; // SUB/ADD
3'b111: alu_ctrl = 4'b0010; // AND
3'b110: alu_ctrl = 4'b0011; // OR
3'b100: alu_ctrl = 4'b0100; // XOR
3'b010: alu_ctrl = 4'b0101; // SLT
3'b001: alu_ctrl = 4'b0110; // SLL
3'b101: alu_ctrl = funct7_5 ?
4'b1000 : 4'b0111; // SRA/SRL
default:alu_ctrl = 4'b0000;
endcase
default: alu_ctrl = 4'b0000;
endcase
end
endmodule

## Slide 8
Immediate Generator — Sign Extension for All Formats
I-type
instr[31:20]
→ ADDI, LW, JALR
sign_ext[31:0]
S-type
instr[31:25] + [11:7]
→ SW, SH, SB
sign_ext[31:0]
B-type
[31][7][30:25][11:8]
→ BEQ, BNE, BLT
sign_ext[31:0]
U-type
instr[31:12] << 12
→ LUI, AUIPC
sign_ext[31:0]
J-type
[31][19:12][20][30:21]
→ JAL
sign_ext[31:0]
SV
module imm_generator (
input logic [31:0] instr,
output logic [31:0] imm_out
);
logic [6:0] opcode;
assign opcode = instr[6:0];
always_comb begin
case (opcode)
// I-type: ADDI, LW, JALR
7'b0010011, 7'b0000011, 7'b1100111:
imm_out = {{20{instr[31]}},
instr[31:20]};
// S-type: SW, SH, SB
7'b0100011:
imm_out = {{20{instr[31]}},
instr[31:25],
instr[11:7]};
// B-type: BEQ, BNE, BLT, BGE
7'b1100011:
imm_out = {{19{instr[31]}},
instr[31],
instr[7],
instr[30:25],
instr[11:8],
1'b0}; // <<1 (word align)
// U-type: LUI, AUIPC
7'b0110111, 7'b0010111:
imm_out = {instr[31:12],
12'b0};
// J-type: JAL
7'b1101111:
imm_out = {{11{instr[31]}},
instr[31],
instr[19:12],
instr[20],
instr[30:21],
1'b0}; // <<1 (word align)
default:
imm_out = 32'b0;
endcase
end
endmodule
💡 B/J types include a left-shift by 1 embedded in the wiring — branch targets are always even addresses

## Slide 9
RISC-V Core — Top-Level RTL Integration
SV
// ─── Top-Level Single-Cycle RISC-V Core ─────────────────────────────────────
module riscv_core (
input logic clk, rst,
// Instruction memory interface
output logic [31:0] imem_addr, // PC → instruction memory
input logic [31:0] imem_rdata, // instruction word from memory
// Data memory interface
output logic [31:0] dmem_addr, // ALU result → data memory address
output logic [31:0] dmem_wdata, // rs2 → data memory write data
output logic dmem_we, // MemWrite control
output logic dmem_re, // MemRead control
input logic [31:0] dmem_rdata // data memory read data → WB mux
);
// ── Internal wires ────────────────────────────────────────────────────────
logic [31:0] pc, pc_next, pc_plus4, branch_tgt, jump_tgt;
logic [31:0] instr;
logic [31:0] rs1_data, rs2_data, wd;
logic [31:0] imm;
logic [31:0] alu_b, alu_result;
logic zero;
logic [3:0] alu_ctrl;
// ── Control signals ────────────────────────────────────────────────────────
logic RegWrite, MemRead, MemWrite, ALUSrc, Branch, Jump, MemToReg;
logic [1:0] ALUOp;
logic branch_taken;
// ── Instruction fetch ──────────────────────────────────────────────────────
assign imem_addr = pc;
assign instr = imem_rdata;
// ── Module instantiations ─────────────────────────────────────────────────
pc_register PC (.clk, .rst, .pc_next, .pc);
pc_adder ADD4 (.pc, .pc_plus4);
control_unit CU (.opcode(instr[6:0]),
.RegWrite, .MemRead, .MemWrite,
.ALUSrc, .Branch, .Jump,
.MemToReg, .ALUOp);
register_file RF (.clk, .rs1(instr[19:15]), .rs2(instr[24:20]),
.rd(instr[11:7]), .we(RegWrite), .wd,
.rd1(rs1_data), .rd2(rs2_data));
imm_generator IG (.instr, .imm_out(imm));
alu_control AC (.ALUOp, .funct3(instr[14:12]),
.funct7_5(instr[30]), .alu_ctrl);
alu ALU (.a(rs1_data), .b(alu_b), .alu_ctrl, .result(alu_result), .zero);
// ── Datapath glue ─────────────────────────────────────────────────────────
assign alu_b = ALUSrc ? imm : rs2_data;
assign branch_taken= Branch & zero;
assign branch_tgt = pc + imm;
assign jump_tgt = pc + imm;
assign pc_next = Jump ? jump_tgt :
branch_taken ? branch_tgt : pc_plus4;
assign wd = MemToReg ? dmem_rdata : alu_result;
// ── Memory interface ──────────────────────────────────────────────────────
assign dmem_addr = alu_result;
assign dmem_wdata = rs2_data;
assign dmem_we = MemWrite;
assign dmem_re = MemRead;
endmodule

## Slide 10
Simulation & Debugging — Testbench and Waveform Analysis
ALU Testbench — SystemVerilog
SV
module tb_alu;
logic [31:0] a, b, result;
logic [3:0] alu_ctrl;
logic zero;
// Instantiate DUT
alu dut (.a,.b,.alu_ctrl,.result,.zero);
// Clock + VCD dump
initial begin
$dumpfile("alu_wave.vcd");
$dumpvars(0, tb_alu);
end
// Test vectors
initial begin
// Test ADD: 15 + 27 = 42
a=32'd15; b=32'd27; alu_ctrl=4'b0000;
#10; assert(result==42 && zero==0)
else $error("ADD FAIL");
// Test SUB: 42 - 42 = 0 (zero=1)
a=32'd42; b=32'd42; alu_ctrl=4'b0001;
#10; assert(result==0 && zero==1)
else $error("SUB/zero FAIL");
// Test AND
a=32'hFF00; b=32'h0FF0; alu_ctrl=4'b0010;
#10; assert(result==32'h0F00)
else $error("AND FAIL");
// Test SLT: 5 < 10 → result=1
a=32'd5; b=32'd10; alu_ctrl=4'b0101;
#10; assert(result==1)
else $error("SLT FAIL");
$display("ALL TESTS PASSED");
$finish;
end
endmodule
Simulation Waveform (GTKWave)
a[31:0]
b[31:0]
ctrl[3:0]
result[31:0]
zero
15
42
FF00
5
27
42
0FF0
10
0
1
2
5
42
0
F00
1
⚡ Debug Checklist
✓ Always check x0 never changes (stays 0)
✓ Verify ALU zero flag triggers branch
✓ Check sign extension for negative immediates
✓ Confirm MemWrite=0 for non-store instructions
✓ Use $display to print register state each cycle

## Slide 11
Simulation Commands — Icarus Verilog & GTKWave Workflow
1. Write RTL Files
# Project structure
├── src/
│ ├── pc_register.sv
│ ├── register_file.sv
│ ├── alu.sv
│ ├── alu_control.sv
│ ├── imm_generator.sv
│ ├── control_unit.sv
│ └── riscv_core.sv
└── tb/
├── tb_alu.sv
└── tb_riscv_core.sv
2. Compile with iverilog
# Compile all RTL + testbench
iverilog -g2012 -o sim.out \
src/*.sv tb/tb_alu.sv
# Check for syntax errors first
iverilog -tnull -g2012 src/alu.sv
# Expected output: no errors
# Any warnings = fix before sim
3. Run Simulation
# Execute simulation
vvp sim.out
# Output example:
# Time=10: a=15 b=27 result=42
# Time=20: a=42 b=42 result=0 zero=1
# ALL TESTS PASSED
# $finish called at time 50
4. View Waveforms
# Open GTKWave
gtkwave alu_wave.vcd &
# In GTKWave:
# 1. File → Open New Tab → alu_wave.vcd
# 2. SST panel: expand tb_alu → dut
# 3. Drag signals: a, b, alu_ctrl,
# result, zero
# 4. Press Ctrl+Shift+F (fit view)
# 5. Use markers to measure timing
5. Synthesize (Vivado)
# Xilinx Vivado TCL flow
create_project riscv ./proj -part xc7a35t
add_files [glob src/*.sv]
set_property top riscv_core [current_fileset]
# Run synthesis
launch_runs synth_1 -jobs 4
wait_on_run synth_1
# Check utilization report
report_utilization -file util.txt
Tip: Coverage
Run both:
• Functional sim
(does it work?)
• Gate-level sim
(after synth,
does timing
hold?)
Use $monitor
for continuous
signal watching

## Slide 12
Day 2 Key Takeaways — What You Should Leave Knowing
01
Single-cycle = one instruction per clock
Every instruction completes in 1 cycle. Simple but slow — critical path = slowest instruction (usually LW).
02
Datapath flows are instruction-specific
Each instruction drives a unique path through the blocks. Opcode selects which path via control signals.
03
Control Unit is purely combinational
Input: opcode[6:0]. Output: 7 control bits + ALUOp[1:0]. No registers — outputs change instantly with opcode.
04
Register File: async read, sync write
Reads are combinational (no clock). Writes need posedge clk + we=1. x0 is always hardwired to zero.
05
ALU drives the zero flag for branches
BEQ computes rs1 - rs2. If result=0, zero=1. Control ORs Branch & zero → branch_taken → PC mux.
06
Immediate generator handles all 5 formats
Each instruction type has a unique bit-scrambling pattern. B and J types include the implicit ×2 shift.
07
Simulate before synthesizing — always
Run all testbenches and confirm waveforms match expected behavior before spending time on FPGA synthesis.
08
Tomorrow: pipelining this design
Day 3 adds 5 pipeline stages, hazard detection, forwarding logic, and data memory cache interface.

## Slide 13
Day 2 Complete
Questions?
💬 Ask anything — PC, RegFile, ALU, Control Unit, testbench. No question is too basic.
Tomorrow — Day 3: Pipeline, Hazards & Memory
▸ Convert single-cycle to 5-stage pipeline (IF/ID/EX/MEM/WB)
▸ Detect and resolve data & control hazards with stalls and forwarding
▸ Add data memory cache interface and branch predictor basics